# Repository Information
1. Name
  1. power_switch_controller
2. Version
  1. 1.0
3. License
  1. BSD, Open-Source Hardware
4. URL
  1. https://github.com/janelia-modular-devices/power_switch_controller.git
5. Author
  1. Peter Polidoro
6. Email
  1. peterpolidoro@gmail.com
## Description
This device controls low-side power switches for turning on and off solenoids, relays, and resistive loads.
# Images
# Usage Instructions
- Connect a power supply to the power switch controller board.
- Connect devices to be switched to the shrouded header connectors on the board with either ribbon cables and IDC connectors or individual 2-pin connectors.
- Connect USB cable to from device to host machine and control over a serial port.
# Build Instructions
- This controller is made from a single 5x3 or 3x2 form factor modular device.
- This device consists of two pcbs, either the (modular_device_base_5x3) and the (power_switch_controller_5x3), or the (modular_device_base_3x2) and the (power_switch_controller_3x2).
- In addition to the two pcbs, there is one acrylic mounting plate (modular_device_enclosure 5x3 enclosure_bottom) or (modular_device_enclosure 3x2 enclosure_bottom).
- Send the zip files containing the gerbers for each of the two pcbs to your favorite pcb manufacturer for fabrication.
- Using the bill of materials and vendor parts lists order the parts necessary for construction for the two pcbs and the mounting plate.
- Assemble each of the pcbs using the assembly instructions provided for each.
- Use the dxf file for the enclosure_bottom to cut the mounting plate from the acrylic sheet using a laser cutter or send the dxf to a laser cutting service for fabrication.
# Hardware
## power_switch_controller_3x2
### Repository Information
1. Name
  1. power_switch_controller_3x2
2. Version
  1. 1.1
3. License
  1. Open-Source Hardware
4. URL
  1. https://github.com/janelia-kicad/power_switch_controller_3x2
5. Author
  1. Peter Polidoro
6. Email
  1. peterpolidoro@gmail.com
Description
This board controls up to 8 low-side power switches for turning on and off solenoids, relays, and resistive loads.
### Images

### Schematic
./hardware/power_switch_controller_3x2/schematic/power_switch_controller_3x2.pdf

### Gerbers
Send gerbers zip file to your favorite PCB manufacturer for fabrication.
./hardware/power_switch_controller_3x2/gerbers/power_switch_controller_5x3_v1.1.zip

### Bill of Materials
PCB Parts
Item	Reference(s)	Quantity	PartNumber	Vendor	Description
1	C1	1	445-4536-1-ND	digikey	CAP CER 10UF 50V 10% X7S 1210
2	C2	1	399-13229-1-ND	digikey	CAP CER 0.1UF 100V X7R 1210
3	D1	1	568-11697-1-ND	digikey	DIODE SCHOTTKY 45V 10A CFP15
4	D2 D3 D4 D5 D6 D7 D8 D9	8	CMHD3595 CT-ND	digikey	DIODE GEN PURP 150V 150MA SOD123
5	L1 L2 L3 L4 L5 L6 L7 L8 L9	9	350-1723-ND	digikey	LED 2MM 24V VERTICAL RED PC MNT
6	MDB1	2	S1011E-16-ND	digikey	16 Position Header Through Hole Male Pins
7	P1	1	CP-063BH-ND	digikey	CONN PWR JACK DC 2.5X5.5 8A T/H
8	P2	1	S9187-ND	digikey	CONN HEADR 2.54MM 16POS GOLD SMD
9	SW1	1	360-2610-ND	digikey	SWITCH SLIDE SPST 0.4VA 28V
10	U1	1	TLE7230RCT-ND	digikey	IC SW SMART OCTAL LOWSIDE PDSO36

1. Supplemental Parts
Item	Quantity	PartNumber	Vendor	Description
1	32	WM2800-ND	digikey	CONN HOUSING 2POS .100 SINGLE
2	64	WM2512-ND	digikey	CONN TERM FEMALE 22-24AWG GOLD
3	64	WM2513-ND	digikey	CONN TERM FEMALE 24-30AWG GOLD
4	4	AKC16H-ND	digikey	CONN IDC SKT 16POS W/POL 15 GOLD
5	1	MC16M-300-ND	digikey	CBL RIBN 16COND 0.050 MULTI 300ft
6	4	APK16B-ND	digikey	CONN IDC PIN 16POS 30AU NO LATCH
7	32	WM2900-ND	digikey	CONN HOUSING 2POS .100 W/LATCH
8	64	WM2570-ND	digikey	CONN TERM FEMALE 22-24AWG GOLD
9	64	WM2572-ND	digikey	CONN SOCKET 24-30AWG CRIMP 30AU
10	32	WM2533-ND	digikey	CONN HOUSING MALE 2POS .100
11	64	WM2566-ND	digikey	CONN PIN 24-30AWG CRIMP 30GOLD
12	64	WM2567-ND	digikey	CONN TERM MALE 22-24AWG GOLD

1. Vendor Parts Lists
  ./hardware/power_switch_controller_3x2/bom/digikey_parts.csv
  ./hardware/power_switch_controller_3x2/bom/supplemental_digikey_parts.csv
### Supplemental Documentation
1. Assembly Instructions
  1. Solder header pins into the driver board, making note of TOP label. Insert header pins on bottom of board so that the long unsoldered header pins point down when the TOP label faces up.
  2. Solder surface mount and through hole components onto the pcb.
## power_switch_controller_5x3
### Repository Information
1. Author
  1. Peter Polidoro
2. License
  1. Open-Source Hardware
# Firmware
## PowerSwitchController
### Library Information
1. Name
  1. PowerSwitchController
2. Version
  1. 2.1.3
3. License
  1. BSD
4. URL
  1. https://github.com/janelia-arduino/PowerSwitchController
5. Author
  1. Peter Polidoro
6. Email
  1. peterpolidoro@gmail.com
Description
Modular device power switch controller library.
### API NAMES
{
  "id": "getApi",
  "result": {
    "firmware": [
      "PowerSwitchController"
    ],
    "verbosity": "NAMES",
    "functions": [
      "setChannelOn",
      "setChannelOff",
      "setChannelsOn",
      "setChannelsOff",
      "toggleChannel",
      "toggleChannels",
      "toggleAllChannels",
      "setAllChannelsOn",
      "setAllChannelsOff",
      "setChannelOnAllOthersOff",
      "setChannelOffAllOthersOn",
      "setChannelsOnAllOthersOff",
      "setChannelsOffAllOthersOn",
      "getChannelsOn",
      "getChannelsOff",
      "getChannelCount",
      "saveState",
      "recallState",
      "addPwm",
      "startPwm",
      "stopPwm",
      "stopAllPwm",
      "setPower",
      "getPowers"
    ],
    "parameters": [
      "channel",
      "channels",
      "state",
      "delay",
      "period",
      "on_duration",
      "count",
      "pwm_index",
      "channel_group",
      "power"
    ],
    "properties": [
      "states"
    ]
  }
}
### API GENERAL
./firmware/PowerSwitchController/api/
### Ancestors
https://github.com/janelia-arduino/ModularServer
https://github.com/janelia-arduino/ModularDeviceBase
### Clients
### Devices
https://github.com/janelia-modular-devices/modular_device_base.git
https://github.com/janelia-modular-devices/power_switch_controller.git
### More Detailed Modular Device Information
https://github.com/janelia-modular-devices/modular-devices
### Installation Instructions
https://github.com/janelia-arduino/arduino-libraries